VIN LAYOUT

123   45	 67   89	10	 11  121314	 151617

AA9   T2	 15    MB   7	   P     (*  *  *)	   0  0  1

1…….Africa

2…….Province

3…….Manufacture Less 500

4/5…..Number of Axles or Axle Make & Number Fitted

6/7…..1st two digit of the GVM

8/9…...Type of Brakes

10…….Year

11…….Plant Area

12/13/14…..VIS (WMI Code)

15/16/17…...Own Sequential Number

Eg:

AA9T215MB7PYB1001

# AA9	:	Receive from SABS

# T2	:	Trailco & 2 Axles

15	:	1500 Kg

# MB	:    Mechanical Brakes

7	:	2007

# P	:	Pretoria

# PY1	:	Receive From SABS if less than 500 Units/year

001	:	First Trailer manufacture that year

## CODES

### Axle				Brake						Year

01 : Single			MB---Mechanical Brakes			2007---7

- : Double			UB---UnBraked				2008---8

03 : Tri 			HB---Hydraulic Brakes			2009---9

VB---Vacuum Brakes			2010---A

CA---Compressed Air			2011---B